## Slide 1
Winthrop
Revere Street Reconstruction Project
September 20, 2022
Project Update
Presented by:
Andrew Valcovic, PE
CHA Consulting, Inc.

## Slide 2: Agenda
Project Overview
History
Goals
Proposed Improvements
Bicycle Accommodations/ Parking impacts
Project Walk-through
Bus Stops
Next Steps
Questions/ Comments?

## Slide 3: Project Overview
Revere Street
  From Magee’s Corner to Crest Avenue
  Includes Signals at each end of the project
  0.5 mile long

## Slide 4: Project Overview
Average Daily Traffic = 15,100 vehicles per day
Vehicle Speeds = 25-30 MPH
(85th Percentile)
Land use
  Primarily residential
  Commercial Areas
  Elementary School - Kennedy Dr.
Funding: MassDOT Transportation Improvement Program (TIP) $6,422,000 Total Construction Cost

## Slide 5: Project Team
Town of Winthrop - Department of Public Works
Project Proponent – Responsible for:
Funding Design, Right-of-Way Acquisitions, Permitting
Consultant Engineering Firm – CHA Consulting
Responsible for Design
MassDOT Highway Division
Responsible for:
Funding Construction, administering the design process, and providing Construction Inspection Services
Federal Highway Administration
Responsible for:
General Oversight
Other Parties
MBTA, Metropolitan Water Resources Commission (MWRA), private utility companies

## Slide 6: Project History
Initial Survey - Fall 2013
  Project included Winthrop Street & Revere Street from Pauline Street to Crest Avenue (0.9 miles)
Initial Public Outreach Meeting – 2014
Transportation Committee Meeting - 2018
25% Design – February 2019
  Scope reduced to just Revere Street (0.5 miles) due to funding & schedule
MBTA Coordination Meeting – January 2020
Design Public Hearing – April 2021
75% Design – July 2021
Currently working on 100% Design

## Slide 7: Project Goals
Improve Safety and Accommodations for all roadway users
  Pedestrians
  Bicycles
  Public Bus Transit
    Route #712 between Orient Heights T Stop and Point Shirley
    10 Bus stops within project limits
  Vehicles
Address Traffic Congestion
  Magee’s Corner
  Revere Street at Crest Avenue/ Highland Avenue
  Kennedy Drive (school drop off/ pick up)
Infrastructure Upgrades
  Poor pavement/ sidewalk condition
  Old stormwater drainage system
  Outdated traffic signal equipment

## Slide 8: Proposed Improvements
Roadway Pavement Reconstruction
Improve Bicycle Accommodations
  Provide 5 ft. wide bike lane while minimizing impacts to parking
Improve Pedestrian Accommodations
  Reconstruct Sidewalks & Curb Ramps for ADA compliancy
  Reduce crosswalk crossing distances at intersections
Typical Section
5’
Bike Lane
5’
Bike Lane
11’
Travel Lane
11’
Travel Lane
5.5’
Sidewalk
5.5’
Sidewalk

## Slide 9: Proposed Improvements
Public Bus Transit
  Relocate bus stops for improved operations and ADA compliancy
Address Areas of Congestion
  Reconstruct Traffic Signals & Geometric Improvements
    Magee’s Corner (Revere Street at Winthrop Street and Main Street)
    Revere Street at Crest Avenue/ Highland Avenue
  Widen Revere Street north of Kennedy Drive to allow for “pull off” shoulder
Replace Stormwater Drainage System
  Deep sump Catch Basins for treatment
New Signage and Pavement Markings

## Slide 10: Proposed Improvements (Bike lanes)

## Slide 11: Proposed Improvements
Improvements
Revere St./ Winthrop St. @ Main St. Intersection
  Replace traffic signal equipment
    Emergency Pre-emption
  Bump out sidewalks
    NW corner
    SE corner

## Slide 12: Proposed Improvements
Bus Stops
  Relocate Bus stops to far side
  New signage
Existing Bus Stop
Future Bus Stop

## Slide 13: Proposed Improvements
Improvements
Stripe Bike lane on western side
Maintain Parking on eastern side
Revere St. @ Shirley St. Intersection
  Add Crosswalk across Shirley St.
  Bump out sidewalk
    SE corner

## Slide 14: Proposed Improvements
Bus Stops
Relocate bus stops away from crosswalks

## Slide 15: Proposed Improvements
Improvements
Add Crosswalk at Locust St.
Widen western shoulder to 8 ft. between Kennedy Dr. and Summit Ave.
Stripe bike lane both sides

## Slide 16: Proposed Improvements
Improvements
Widen western shoulder to 8 ft. between Kennedy Dr. and Summit Ave.
Stripe bike lane both sides

## Slide 17: Proposed Improvements
Bus Stops
Relocate NB bus stop from Summit Ave. to Locust St
Relocate SB bus stop away from Summit Ave.

## Slide 18: Proposed Improvements
Improvements
Stripe bike lane both sides
  Buffered bike lane on east side north of Hutchinson Ave.
Widen sidewalk (2’ +/-) between Hutchinson Ave. and Crest Ave.

## Slide 19: Proposed Improvements
Bus Transit Stops
Relocate SB bus stop to far side of Golden Dr.
Maintain NB bus stop on near side of Hutchinson Ave.
  Widen sidewalk at bus stop.

## Slide 20: Proposed Improvements
Improvements
Replace traffic signal equipment
Widen Revere St. NB approach
Reconstruct islands
Two-stage-turn-queue-boxes for bicycle left turns
Bump out sidewalks
  NW corner, NE corner, SW corner
Reconstruct Quincy Avenue Path pavement

## Slide 21: Proposed Improvements
Bus Stops
Relocate NB bus stop to far side along Crest Ave.
Relocate SB bus stop away from intersection.

## Slide 22: Next Steps
100% Design – October 2022
Right-of-Way Acquisition – September 2022 to May 2023
Advertise Project for Bids – June 2023
Construction begins - Spring 2024
Construction complete - November 2025

## Slide 23: Questions/ Comments
Questions/ comments may also be sent to:
Steven R. Calla
Director of Public Works
(617) 846-1341
scalla@town.Winthrop.ma.us